## Slide 1: Michael Gassner, Titus Cieslewski, Davide Scaramuzza
Dynamic Collaboration without Communication:
Vision-Based Cable-Suspended Load Transport with Two Quadrotors
Notes: Uni ZH!
Read the title slower

## Slide 2: Problem Statement
Transport a load that is too heavy for just one quadrotor
Should be as simple as possible
How do humans do it?
Not much explicit communication is needed!
Friends – The one with the cop
T. Cieslewski – University of Zurich – Dynamic Collaboration without Communication
Notes: Transport too heavy
In a simple; simplest
Humans? adapts
No comm!

## Slide 3: Leader-Follower Approach
Split control over degrees of freedom among robots
  Leader controls of the load
  Follower controls of the load
Eliminate any necessity for communication: Make follower passive!
  : Track altitude of leader
  : Don’t move laterally
T. Cieslewski – University of Zurich – Dynamic Collaboration without Communication
Notes: Split DoF
How
Eliminate necessity for comm: Passive follower. How?

## Slide 4: Perception
Both quadrotors: Downlooking fisheye for pose estimation and object gripper tracking
Follower: Forward looking pinhole for leader tracking
Fully on-board state estimation with vision and IMU
T. Cieslewski – University of Zurich – Dynamic Collaboration without Communication

## Slide 5: LQR Slung-load Control
Follower tracks leader’s altitude and moving direction with visual servoing
Leader and follower control load gripper pose as if it were a single slung-load.
Follower only controls lateral position
Reducing oscillations for robustness
T. Cieslewski – University of Zurich – Dynamic Collaboration without Communication
Notes: 1. Gripper tracking (expand more; add side view of quads + cameras/vision)
2. Leader tracking

## Slide 6: Summary
Collaborative load transport
No communication or explicit relative localization needed!
Everything is done fully on-board using only vision and IMU
Quantitative results presented at interactive session
T. Cieslewski – University of Zurich – Dynamic Collaboration without Communication
Notes: Move vision ahead!